## Slide 1
領先創新·
·超越自我
2019 Synopsys ARC盃電子設計競賽

## Slide 2: SMART FIREFIGHTER
UETer: DANG Hai Ninh & VU Huong Giang
SISLAB VNU University of Engineering and Technology (VNU – UET)
August 2019

## Slide 3: Agenda
Motivation and objectives
Design implementation
Test Results
Summary

## Slide 4: Agenda
Motivation and objectives
Design implementation
Test Results
Summary

## Slide 5: Motivation
Fire growing rate are exponential
Quick methods to identify and extinguish fire save lives and properties

## Slide 6: Motivations (cont.)
Smoke sensor:
Slow detection
No location of flame
Wide water spray nozzle:
Waste water
Causing damage to other furniture
Smart firefighter
Quick and accurate detection of flame location.
Spray water flow to the fire correctly, while keeping other areas dry spear.
Can be mobility.
Expensive
Fire extinguisher
Heavy
Limited visibility
Traditional methods

## Slide 7: Our objective: low-cost smart fight fighter
Autonomously detect and extinguish the fire
Useful in certain types of incidents where the environment will be very dangerous for the humans
Warning of danger, usually a loud noise
Fire detection: Low-cost InfraRed Sensors
3D-printed robot arm
ARC EM Starter kit for algorithms & controls

## Slide 8: Agenda
Motivation and objectives
Design implementation
Test Results
Future plan
Summary

## Slide 9: Processing flow
Start
IR camera send hottest pixel to EMSK
EMSK calculates the distance to the heat source and determines "IS IT A FIRE?”
YES
The two axis robot arm sprays water to put out the fire
NO

## Slide 10: System components
2x thermal sensor 32x24 pixel
FOV: 55°x35°
Water pump
2 axis robot arm
2 stepper motor
H bridge
UART
UART
Flame directions
Flame directions
Calculate flame locations
Spray water
Move spray nozzle
ARC EM Starter Kit
Two Low-cost Infrared sensors
3D printed robot hands controlled by step motors
One water pump

## Slide 11: Flame Detection
Flame location: (Fx, Fy, )
calculated from sensor data
Fx and Fy: solved by trigonometric calculation
Hottest pixel: xh = 2, yh = 1
- X angle:  = (55/32)*xh
- Y angle:  = (35/24)*yh
- 2 sensor: 1, 2, 1, 2
Angle calculation from sensors
Detection range: 4mx4.4mx4.4m

## Slide 12: 3D-printed robot hand for spraying water
  Planetary Gears
  12v High pressure pump

## Slide 13: ARC EM Starter Kit connection
  J3 : 2 Stepper driver module.
  J1 & J5 : 2 IR camera module (using UART).
  J6 : Relay module for water pump control

## Slide 14: Agenda
Motivation and objectives
Design implementation
Test Results
Future plan
Summary

## Slide 15: Demonstration setup

## Slide 16: Test Results – Candle flame visualization
1m
2m
3m

## Slide 17: Agenda
Motivation and objectives
Design implementation
Test Results
Future plan
Conclusion

## Slide 18: Conclusions
Fire grows very fast in home environment
Industrial Smart Fight Fighter are expensive
Our proposal: Low-cost Smart Fight Fighter
  Low-cost IR sensor for fire detection
  3D-Printed Robot hands for water control for extinguishing fire
  ARC EM Starter Kit for algorithm development & control
Future work
  Multi-sensor nodes with wireless connections
  Embedded AI for fire classification

## Slide 20
1
2
Fx
Fy
Ground
50cm
40cm
IR sensor
IR sensor

## Slide 21
Sensor wall
1
2
Fx
Fy
50cm
40cm
IR sensor
IR sensor
Ground